## Slide 1: Last Level Collective Hardware Prefetching For Data-Parallel Applications
George Michelogiannakis, John Shalf
Lawrence Berkeley National Laboratory,
Berkeley, CA, USA
HiPC 2017

## Slide 2: Overview
Last-level cache (LLC) prefetcher that exploits data-parallel application memory access patterns
  Uses one core’s accesses to predict for other cores
Can prefetch from multiple memory pages with one activation
Compared to well-established competition
  5.5% execution time improvement by average
  DRAM bandwidth increase 9% to 18%
  27% more timely prefetches
  25% increased coverage

## Slide 3: Data-Parallel Applications
3D space
Slice into 2D planes
2D plane
still too large for single processor
Divide array into tiles
One tile per processor
Sized for L1 cache
(just one example)
Notes: The loop shown is just one example. Can also be done with cache coherency.

## Slide 4: Observation: Access Patterns Are Correlated
Once the first core requests a tile, lets prefetch the rest of them
Notes: Based on the loop shown, one core requesting a tile is a strong indication that another core will request a tile soon.

## Slide 5: Memory Address Order
DRAM throughput drops 25% for loads and 41% for stores [1] for out-of-order accesses versus in-order
  Power increases 2.2x for reads and 50% for stores
[1] Collective Memory Transfers for Multi-Core Chips. ICS 2014
0
N-1
N
2N-1
Challenge: memory page boundaries
Notes: Prefetching as shown not all prefetchers can do, requires higher-level cache prefetching to have a global view, but even then crossing memory page boundaries is expensive.

## Slide 6: LLCP: Collective Prefetcher
Prefetcher that detects correlation of data-parallel applications and preserves memory address order across memory pages
Based on strided prefetcher (strides work well for tiles)
Base
0
N-1
N
2N-1
1
2
Base + stride
Base + 2stride
3
4
5
6
Stride prefetcher entry
Notes: One entry has a base and a stride among other things such as confidence. But applying a strided prefetcher in a L1 cache can’t prefetcher in order. Applying the strided prefetcher in the LLC could potentially but this is sensitive to the time requests come in, and the memory page boundary problem remains.

## Slide 7: LLCP: Merge Strides of Different Cores
Base
Base + stride
Base + 2stride
Base
Base + stride
Base + 2stride
Core 1 stride entry
Core 2 stride entry
Notes: The goal is to relate these entries such that when one activates both activate. But in memory address order.

## Slide 8: LLCP: Merge Strides of Different Cores
0
N-1
N
2N-1
1
4
2
5
3
6
Base1
Base2
Base1 + stride
Base2 + stride
Base1 + 2stride
Base2 + 2stride
This is a stride group
Activating one entry activates the rest
Notes: This way all stride entries in the group activate and the memory experiences requests in address order.

## Slide 9: Crossing Memory Page Boundaries
LLC prefetchers typically operate on the physical address space
Each stride entry can be in a different memory page than the rest
LLCP activates multiple stride entries from one memory access, therefore one prefetch spans memory address pages
0
N-1
N
2N-1
1
4
2
5
3
6
Notes: Each stride entry can potentially be in a different memory page. By relating them and activating multiple entries, one prefetch activation spans many memory pages.

## Slide 10: Architecture
Stride table
Address
Base
Base + Nstride
…
Group table
PC of request
Stride entries also include a pointer to
other stride entries of the group
First stride entry of group
No cycle time increase compared to strided
Higher dynamic power compared to competitors
But only a 1% compared to a L2 cache
Notes: These tables are accessed in parallel. The left table is exactly like the original strided prefetcher. The one on the right points to the first entry of a group, if one exists. Then the other entries are found because entries in a group are organized as a linked list. By traversing this list memory requests in address order are generated.

## Slide 11: Operation
Memory request arrives
Stride entry exists?
Create entry. No group activation
Conf > threshold?
No
Yes
Update confidence. No group activation
No
Group exists?
Yes
No
Yes
Prefetch entire group
Prefetch entry. No group activation
Notes: Flow diagram showing the algorithmic function of LLCP. Only the bottom left is really new compared to the original strided prefetcher.

## Slide 12: Methodology
Gem5 simulator with a collection of Parsec, Rodinia, and Parboil benchmarks to represent different memory access patterns
64 in-order (later out of order) ALPHA cores, 64KB L1 caches, four 32MB shared L2 caches, MESI.
Compare against strided prefetcher in Gem5, global history buffer [3], and spatial memory streaming [2]
Prefetchers are sized individually for comparable area
[2] S. Somogyi et al., “Spatial memory streaming,” ser. ISCA ’06, 2006
[3] K. J. Nesbit and J. E. Smith, “Data cache prefetching using a global history buffer,” ser. HPCA, 2004
Notes: Our benchmarks show different patterns, including those that hurt LLCP. Cache sizes are reasonable based on industrial designs. Prefetcher size depends mostly on the tables they contain for their purpose.

## Slide 13: Execution Time
Chart: Speedup compared to no prefetching (%)
| Backprop | Cutcp | Heartwall | Myocyte | Stencil | Streamcluster | Ferret | Fluidanimate | Average
Stride | 9.261 | 6.4442 | 1.8483 | 16.1689 | 9.0067 | 3.9972 | -4.1995 | 4.8321 | 5.9198
SMS | 1.6029 | 7.0192 | -0.068479 | -1.0649 | 0.44037 | 0.99171 | -0.031292 | 0.9877 | 1.2347
GHB | 6.6329 | 1.1022 | -0.43167 | -1.1795 | 15.4652 | 0.34354 | -4.6154 | 0.0022374 | 2.1649
LLCP | 8.0876 | 12.1972 | 1.9409 | 24.4799 | 13.0917 | 4.276 | 0.21258 | 8.4126 | 9.0873
5%
9%
2%
1%
Notes: By average we improve. But notice that in Backprop and Stencil LLCP does worse than one competitor. LLCP is prone to lower accuracy and thrashing in benchmarks that either change their memory access patterns or mimic one to fool LLCP. Note that LLCP can be can be configured individually for each benchmark to fix that, but for fairness in a general-purpose system we used the same configuration for all benchmarks.
In most bechmarks though LLCP does better than competition.

## Slide 14: Other Metrics
Improvement over best competitor (which one differs by metric)
Timeliness: Number of prefetches squashed by demand misses over total number of prefetches
Coverage: Referenced prefetched data over number of cache misses
Accuracy: Referenced prefetched data over total prefetched data
Metric | Improvement
LLC miss rate | 44%
DRAM read b/w | 9%
DRAM row buffer hit rate | 5%
LLC read miss latency | 15%
Timeliness | 17%
Coverage | 25%
Accuracy | -8% to 22%
Notes: These numbers explain the results right before. Miss rate reduction is a major benefit, related to timeliness. DRAM read b/w, row buffer hit rate, and LLC read miss latency are a direct improvement from in-order memory access. Timeliness makes sense that we improve because we prefetch more data from a single memory request and thus data are more likely to be already prefetched when a core requests it. Coverage improvement also makes sense for the same reason. Accuracy can be lower but is usually higher. This also makes sense because lower accuracy is caused by thrashing, fetching useless data, and prematurely evicting useful data. In applications that fool LLCP, this is a possibility.

## Slide 15: Out of Order Cores and Discussion
LLCP gains increase with OOO cores
  OOO cores stress memory bandwidth
Smaller LLC sizes reduce LLCP gains
  Larger LLCs increase gains
L1 prefetchers do not close the gap
  Cannot replicate LLCP functionality
LLCP can be configured to be more or less aggressive
Notes: In-order cores care about memory latency. OOO cores care about memory bandwidth. LLCP improves both based on memory access in order.
Smaller LLCs reduce LLCP gains because they make thrashing (kicking out useful data by prefetching too much data) more likely.
L1 prefetchers don’t have a global view. Other LLC prefetchers are challenged by crossing page boundaries.
There are multiple configuration parameters in LLCP. Refer to the paper.

## Slide 16: Conclusion
LLCP exploits data-parallel memory access patterns to improve performance
  Prefetch from multiple memory pages from a single activation
  Access DRAM in memory address order
Compared to competition
  5.5% execution time improvement by average
  DRAM bandwidth increase 9% to 18%
  27% more timely prefetches
  25% increased coverage
Questions?