## Slide 1: Extending Summation Precision for Network Reduction Operations
George Michelogiannakis,
Xiaoye S. Li, David H. Bailey, John Shalf
Computer Architecture Laboratory
Lawrence Berkeley National Laboratory

## Slide 2: Background
64-bit double-precision variables are not precise enough for many operations, such as summations with billions of operands
  Because of the limited mantissa bits
Value = Mantissa x 2(Exp – 1023 – 52)
1 + 1 = 2 but 2100 + 1 = 2100

## Slide 3: Background
Precision loss has been cited as an important problem
  Insufficient precision, or different results on different machines
Researchers have resorted to increased or infinite precision libraries
Add 10-8 to 108

## Slide 4: Related Work and Motivation
Intra-node (local processor) computations have a wealth of work:
  Sorting or recursion techniques
  Software libraries that offer increased or infinite precision
  Fixed-point integer representations with hardware support
We focus on distributed summations which occur with a tree-like communication pattern, such as MPI_reduce
A+B
A
B
C+D
C
D
A+B+C+D

## Slide 5: Challenges
In a distributed system, sorting and recursion techniques incur too much communication
Increased precision libraries still not enough
Past work has shown the benefits of doing computation in the NIC without invoking the local processor [1]
  NICs have limited programmable logic
  Complex data structures for arbitrary precision libraries are infeasible
NIC
CPU
Network
[1] F. Petrini et al., “NIC-based reduction algorithms for large-scale clusters,” International Journal on High Performance Computer
Networks, vol. 4, no. 3/4, pp. 122–136, 2006.

## Slide 6: Big Integers
Our solution to enable in-NIC computation with no precision loss:

## Slide 7: Big Integer Expansions
To represent the same number space as a double-precision variable, we can use a 2101-bit wide fixed-point integer variable
Advantages:
  No precision loss
  Reproducibility
  Simple integer arithmetic
Similar wide integers have been applied to intra-node computations [2]
[2] U. Kulisch, “Very fast and exact accumulation of products,” Computing, vol. 91, no. 4, pp. 397–405, 2011.

## Slide 8: Mapping from Double Variables
Simply shifting the mantissa according to the exponent’s value

## Slide 9: Applicability to Network Operations
Past work has applied in-NIC computations only for double-precision variables
Can’t apply increased or infinite precision libraries
  Programmable logic is limited. For example, Elan3 in Quadrics Qsnet provides a 100MHz RISC processor
  Adding dedicated hardware for fully-functional floating point hardware is costly and risky
BigInts make in-NIC computation without precision loss feasible
  BigInts require simple integer arithmetic
  Tensilica library FPUs use 150,000 gates. Equivalent integer adder uses 380 gates

## Slide 10: In-NIC Computations With BigInts
Advantages:
  Local processor is not woken up from potentially deep sleep
  NIC to processor interconnect not stressed
  Simple dedicated hardware or programming logic support
Result: Latency and energy benefits
  Past work has quoted up to 121% speedup for in-NIC reductions [3]
  While avoiding any precision loss
[3] F. Petrini et al., “NIC-based reduction algorithms for large-scale clusters,”
International Journal on High Performance Computer Networks, vol. 4, no. 3/4, pp. 122–136, 2006.

## Slide 11: Evaluation
Communication latency
Computation time
Precision gain

## Slide 12: Communication Latency
For such small payloads, latency is dominated by fixed costs
35% increase versus doubles. 2%-14% compared to double-doubles
50,000 reductions
One reduction
operation at
a time (operations
are not pipelined)

## Slide 13: Computation Time
Modern Intel FPUs require 5 cycles
Increased precision representation may need much more
  Double-doubles require 20 operations for a single addition
BigInts match the 5 cycles with a 424-bit integer adder
Integer adder to support Infiniband 4x EDR theoritical peak rate (100 Gb/s) need only be 32 bits operating at 0.6 GHz
This requires 380 gates
  Simple FPUs from the Tensilica library use 150,000 gates
In-NIC computation avoids context switching (μs) and waking up the processor from deep sleep (potentially seconds)

## Slide 14: Arc Length of Irregular Function
We calculate the arc length of
The arc length calculation sums many highly varying quantities

## Slide 15: Arc Length of Irregular Function
Digit comparison after expressing results in decimal form
BigInt has no precision loss
To focus on the network, we assume no precision loss in local-node computations

## Slide 16: Composite Summation
Adding operands of 10-8 to 108
BigInt equals the analytical result
To focus on the network, we assume no precision loss in local-node computations

## Slide 17: Geometric Series
We calculate:
The answer should never be 2
  Doubles report 2 for k > 53
  Long doubles for k > 64
  Double-doubles for k > 106
  BigInts for k > 1024
    After k > 1024, the numbers are outside the double-precision variable number space

## Slide 18: Conclusions
Precision loss in large system-wide operations can be a significant concern
Previously, reduction operations without precision loss could not be performed in the NICs
Wide fixed-point (integer) representations enable this with very simple hardware
  Cheap and fast computation without precision loss
BigInts complement intra-node (local processor) techniques

## Slide 19: Questions?