## Slide 1: Hardware Support for Collective Memory Transfers in Stencil Computations
George Michelogiannakis, John Shalf
Computer Architecture Laboratory
Lawrence Berkeley National Laboratory

## Slide 2: Overview
This research brings together multiple areas
  Stencil algorithms
  Programming models
  Computer Architecture
Purpose: Develop direct hardware support for hierarchical tiling constructs for advanced programming languages
  Demonstrate with 3D stencil kernels

## Slide 3: Chip Multiprocessor Scaling
Intel 80-core
NVIDIA Fermi: 512 cores
By 2018 we may witness 2048-core chip multiprocessors
AMD Fusion:
four full CPUs
and 408 graphics
cores
How to stop interconnects from hindering the future of computing. OIC 2013

## Slide 4: Data Movement and Memory Dominate
Chart: PicoJoules
| DP FLOP | Register |  | 1mm on-chip |  | 5mm on-chip |  | Off-chip/DRAM |  | local interconnect |  | Cross system |
now | 100 | 100 | 3.5 | 3.5 | 6 | 6 | 30 | 30 | 2000 | 2000 | 2500 | 2500 | 3000 | 3000
2018 | 25 | 25 | 1.5 | 1.5 | 6 | 6 | 30 | 30 | 850 | 850 | 1000 | 1000 | 1500 | 1500
Exascale computing technology challenges. VECPAR 2010
Now: 45nm technology
2018: 11nm technology

## Slide 5: Memory Bandwidth
Wide variety of
applications
are memory
bandwidth bound

## Slide 6: Collective Memory Transfers

## Slide 7: Computation on Large Data
3D space
Slice into 2D planes
2D plane still too large for
a single processor

## Slide 8: Domain Decomposition Using Hierarchical Tiled Arrays
Divide array into tiles
One tile per processor
L1 cache or local store
CPU
Tiles are sized for
processor local
(and fast) storage

## Slide 9: The Problem: Unpredictable Memory Access Pattern
MEM
Req
Req
Req
Req
Req
Req
Req
Req
Req
One request per tile line Different tile lines have different memory address ranges
0
N-1
N
2N-1
One request
Row-major mapping

## Slide 10: Random Order Access Patterns Hurt DRAM Performance and Power
Tile line 1
Tile line 2
Tile line 3
Tile line 4
Tile line 5
Tile line 6
Tile line 7
Tile line 8
Tile line 9
Reading tile 1 requires row activation and copying
Tile line 1
Tile line 2
Tile line 3
Tile line 1
Tile line 2
Tile line 3
In order requests:
3 activations
Worst case:
9 activations

## Slide 11: Collective Memory Transfers
MEM
Req
Req
Requests replaced with one collective request
Reads are presented sequentially to memory
0
N-1
N
2N-1
5
1
2
3
4
The CMS engine takes control of the collective transfer

## Slide 12: Execution Time Impact
Up to 32% application execution time reduction
2.2x DRAM power reduction for reads. 50% for writes
8x8 mesh
Four memory controllers
Micron 16MB 1600MHz
modules with a
64-bit data path
Xeon Phi processors

## Slide 13: Relieving Network Congestion

## Slide 14: Hierarchical Tiled Arrays
“The hierarchically tiled arrays programming approach”. LCR 2004

## Slide 15: Questions for You
What do you think is the best interface to CMS from the software?
  A library with an API similar to the one shown?
  Left to the compiler to recognize collective transfers?
How would this best work with hardware-managed caches?
  Prefetchers may need to recognize collective operations
This work seems to indicate that collective transfers are a good idea for memory bandwidth and network congestion
  Any other areas of application?

## Slide 16: CMS Engine Implementation
ASIC Synthesis | DMA | CMS
Combinational area (μm2) | 743 | 16231
Non-combinational area (μm2) | 419 | 61313
Minimum cycle time (ns) | 0.6 | 0.75
To offset the cycle time increase, we can add a pipeline stage
CMS significantly simplifies the memory controller because
shorter FIFO-only transaction queues are adequate