## Slide 1: A Generalized Framework for Auto-tuning Stencil Computations
Shoaib Kamil1,3, Cy Chan4, Samuel Williams1,
Leonid Oliker1, John Shalf1,2, Mark Howison3,
E. Wes Bethel1, Prabhat1
1Lawrence Berkeley National Laboratory (LBNL)
2National Energy Research Scientific Computing Center (NERSC)
3EECS Department, University of California, Berkeley (UCB)
4CSAIL, Massachusetts Institute of Technology (MIT)
SAKamil@lbl.gov

## Slide 2: The Challenge: Productive Implementation of an Auto-tuner

## Slide 3: Conventional Optimization
Take one kernel/application
  Perform some analysis of it
  Research the literature for appropriate optimizations
  Implement a couple of them by hand optimizing for one target machine.
  Iterate a couple of times.
Result:
improve performance for one kernel on one computer.

## Slide 4: Conventional Auto-tuning
Automate the code generation and tuning process.
  Perform some analysis of the kernel
  Research the literature for appropriate optimizations
  implement a code generator and search benchmark
  explore optimization space
  report best implementation/parameters
Result:
significantly improve performance for one kernel on any computer.
i.e. provides performance portability
Downside:
  autotuner creation time is substantial
  must reinvent the wheel for every kernel

## Slide 5: Generalized Frameworks for Auto-tuning
Integrate some of the code transformation features of a compiler with the domain-specific optimization knowledge of an auto-tuner
  parse high-level source
  apply transformations allowed by the domain, but not necessarily safe based on language semantics alone
  generate code + auto-tuning benchmark
  explore optimization space
  report best implementation/parameters
Result:
significantly improve performance for any kernel on any computer for a domain or motif.
i.e. performance portability without sacrificing productivity

## Slide 6: Outline
Stencils
Machines
Framework
Results
Conclusions

## Slide 7: Benchmark Stencils
  Laplacian
  Divergence
  Gradient
  Bilateral Filtering

## Slide 8: What’s a stencil ?
Nearest neighbor computations on structured grids (1D…ND array)
stencils from PDEs are often a weighted linear combination
of neighboring values
cases where weights vary in space/time
stencil can also result in a table lookup
stencils can be nonlinear operators
caveat: We only examine implementations like Jacobi’s Method
(i.e. separate read and write arrays)
i,j,k
i+1,j,k
i-1,j,k
i,j+1,k
i,j,k+1
i,j,k-1
i,j-1,k

## Slide 9: Laplacian Differential Operator
7-point stencil on scalar grid, produces a scalar grid
Substantial reuse (+high working set size)
Memory-intensive kernel
Elimination of capacity misses may improve performance by 66%
xy product
write_array[ ]
x dimension
read_array[ ]
u’
u
i,j,k
i+1,j,k
i-1,j,k
i,j+1,k
i,j,k+1
i,j,k-1
i,j-1,k

## Slide 10: Divergence Differential Operator
6-point stencil on a vector grid, produces a scalar grid
Low reuse per component.
Only z-component demands a large working set
Memory-intensive kernel
Elimination of capacity misses may improve performance by 40%
read_array[ ][ ]
x dimension
write_array[ ]
xy product
x
y
z
u
i+1,j,k
i-1,j,k
i,j+1,k
i,j,k+1
i,j,k-1
i,j-1,k

## Slide 11: Gradient Differential Operator
6-point stencil on a scalar grid, produces a vector grid
High reuse (like laplacian)
High working set size
three write streams (+ write allocation streams) = 7 total streams
Memory-intensive kernel
Elimination of capacity misses may improve performance by 30%
write_array[ ][ ]
x dimension
read_array[ ]
xy product
x
y
z
u
i+1,j,k
i-1,j,k
i,j+1,k
i,j,k+1
i,j,k-1
i,j-1,k

## Slide 12: 3D Bilateral Filtering
Extracted from a medical imaging application (MRI processing)
Normal Gaussian stencils smooth images,
but destroy sharp edges.
This kernel performs anistropic filtering thus preserving edges.
We may scale the size of the stencil (radius=3,5)
  73-pt or 113-pt stencils.
  apply to dataset of 192 x 256x256 slices
  originally 8-bit grayscale voxels, but processed as 32-bit floats

## Slide 13: 3D Bilateral Filtering (pseudo code)
Each point in the stencil mandates a voxel-dependent indirection,
and each stencil also requires one divide.
for all points (xyz) in x,y,z{
voxelSum = 0
weightSum = 0
srcVoxel = src[xyz]
for all neighbors (ijk) within radius of xyz{
neighborVoxel = src[ijk]
neighborWeight = table2[ijk]*table1[neighborVoxel-srcVoxel]
voxelSum +=neighborWeight*neighborVoxel
weightSum+=neighborWeight
}
dstVoxel = voxelSum/weightSum
}
Large radii results in extremely compute-intensive kernels with large working sets

## Slide 14: Benchmark Machines

## Slide 15: Multicore SMPs
Experiments only explored parallelism within an SMP
We use a Sun X2200 M2 as a proxy for the XT5 (e.g. Jaguar)
We use a Nehalem machine as a proxy for possible future Cray machines.
Barcelona/Nehalem are NUMA
AMD Budapest (XT4)
AMD Barcelona (X2200 M2)
Intel Nehalem (X5550)

## Slide 16: Generalized Framework for Auto-tuning Stencils
Copy and Paste auto-tuning

## Slide 17: Overview
Given a F95 implementation of an application:
Programmer annotates target stencil loop nests
Auto-tuning System:
  converts FORTRAN implementation into internal representation (AST)
  builds a test harness
  Strategy Engine iterates on:
    apply optimization to internal representation
    backend generation of optimized C code
    compile C code
    benchmark C code
  using best implementation, automatically produces a library for that kernel/machine combination
Programmer then updates application to call optimized library routine

## Slide 18: Strategy Engine: Auto-parallelization
The strategy engines can auto-parallelize cache blocks among hardware thread contexts.
We use a single-program, multiple-data (SPMD) model implemented with POSIX Threads (Pthreads).
All threads are created at the beginning of the application.
We also produce an initialization routine that exploits the first touch policy to ensure proper NUMA-aware allocation.

## Slide 19: Strategy Engine: Auto-tuning Optimizations
Strategy Engine explores a number of auto-tuning optimizations:
  loop unrolling/register blocking
  cache blocking
  constant propagation / common subexpression elimination
Future Work:
  cache bypass (e.g. movntpd)
  software prefetching
  SIMD intrinsics
  data structure transformations

## Slide 20: Experimental Results
NOTE: threads are ordered to exploit:
multiple threads within a core (Nehalem only),
then multicore,
then multiple sockets (Barcelona/Nehalem)

## Slide 21: Laplacian Performance
On the memory-bound architecture (Barcelona), auto-parallelization doesn’t make a difference.
Auto-tuning enables scalability.
Barcelona is bandwidth-proportionally faster than the XT4.
Nehalem is ~2.5x faster than Barcelona, and 4x faster than the XT4
Auto-parallelization plus tuning significantly outperforms OpenMP.
Auto-tuning
Auto-
parallelization
serial
reference
OpenMP
Comparison
Auto-NUMA

## Slide 22: Divergence Performance
No changes to the framework were required (just drop in F95 code)
As there was less reuse in the Divergence than in Laplacian, there are fewer capacity misses.
So auto-tuning has less to improve upon
Nehalem is ~2.5x faster than Barcelona
Auto-tuning
Auto-
parallelization
serial
reference
OpenMP
Comparison
Auto-NUMA

## Slide 23: Gradient Performance
No changes to the framework were required (just drop in F95 code)
Gradient has moderate reuse, but a large number of output streams.
Performance gains from auto-tuning are moderate (25-35%)
Parallelization is only valuable in conjunction with auto-tuning
Auto-tuning
Auto-
parallelization
serial
reference
OpenMP
Comparison
Auto-NUMA

## Slide 24: 3D Bilateral Filter Performance (radius=3)
No changes to the framework were required (just drop in F95 code)
Essentially a 7x7x7 (343-pt) stencil
Performance is much more closely tied to GHz
instead of GB/s.
Auto-parallelization yielded near perfect parallel efficiency
wrt cores on Barcelona/Nehalem (Nehalem has HyperThreading)
Auto-tuning significantly outperformed OpenMP (75% on Nehalem)
Auto-tuning
Auto-
parallelization
serial
reference
OpenMP
Comparison

## Slide 25: 3D Bilateral Filter Performance (radius=5)
basically the same story as radius=3
XT4/Nehalem delivered approximately same performance as they did with radius=3
Barcelona delivered somewhat better performance.
Auto-tuning
Auto-
parallelization
serial
reference
OpenMP
Comparison

## Slide 26: Summary

## Slide 27: Summary: Framework for auto-tuning stencils
Dramatic step forward in auto-tuning technology
Although the framework required substantial up front work,
it provides performance portability across the breadth of architectures AND stencil kernels.
Delivers very good performance, and well in excess of OpenMP.
Future work will examine relevant optimizations
  e.g. cache bypass would significantly improve gradient performance.

## Slide 28: Summary: Machine Comparison
Barcelona delivers bandwidth-proportionally better performance on the memory-intensive differential operators.
Surprisingly, Barcelona delivers ~2.5x better performance on the compute intensive bilateral filter.
Nehalem clearly sustains dramatically better performance than either Opteron.
Despite having a 15% faster clock, nehalem realizes a much better bilateral filter performance.

## Slide 29: Acknowledgements
Research supported by DOE Office of Science under contract number DE-AC02-05CH11231
Microsoft (Award #024263)
Intel (Award #024894)
U.C. Discovery Matching Funds (Award #DIG07-10227)
All XT4 simulations were performed on the XT4 (Franklin) at the National Energy Research Scientific Computing Center (NERSC)

## Slide 30: Questions?